## Slide 1: Model-driven service design
Introduction
Roque Gagliano

## Slide 2: What is a service?
Notes: The word “service” is

## Slide 3: Let’s start from the top…we have a customer
Resources:
You
Network
Compute
Storage
Network Functions (firewall, DPI, load balancer, etc)

## Slide 4: Let’s start from the top…we have a customer Which consumes products
Resources:
Network
Compute
Storage
Network Functions (firewall, DPI, load balancer, etc)
Products
Fullfilment
Assurance
Others (strategy, billing,…)
Notes: Service Fullfilment: Is the process Order-to-Service

## Slide 5: Let’s start from the top…we have a customer Which consumes products
Resources:
Network
Compute
Storage
Network Functions (firewall, DPI, load balancer, etc)
Products
Fullfilment
Assurance
Others (strategy, billing,…)
Our focus
Multi-domain
Multi-vendor
Examples:

## Slide 6
Self-service portal
Call center
Products & Price Catalog
Order capture engine
Customers & accounts
Product configuration
Order Management
Service provisioning
Service activation
Supply Chain
Field Service
Installed assets
Billing
Customer care
Knowledge
base
Contracts & SLAs
CPQ
Service Fulfillment and related parts of OSS/BSS (except Service Assurance)
Resource inventory
Notes: CPQ = Configure, Price and Quote

## Slide 7
Self-service portal
Call center
Products & Price Catalog
Order capture engine
Customers & accounts
Product configuration
Order Management
Service provisioning
Service activation
Supply Chain
Field Service
Installed assets
Billing
Customer care
Knowledge
base
Contracts & SLAs
CPQ
Service Fulfillment and related parts of OSS/BSS (except Service Assurance)
Resource inventory
Layers
Responsible
For
Network
Services
Notes: CPQ = Configure, Price and Quote

## Slide 8: Network Services
Service offered by the network to be consumed by other business layers (for example to create a product)
Examples:
  SP: E-Line, VPN, 4G mobile data, etc.
  Enterprise/DC: New employee IT, server-network-activation
Network services typically spans multiple domains (optical, IP, DC, mobile, etc.)
A single network element MAY support multiple services
Note: the term “Network Service” is also overused across the board by standard and industry groups.

## Slide 9: Provisioning and Activation layer exposes different “type” of services: customer and resource facing
Resources:
Order Capture and Management + BSS + Inventories
Network
Compute
Storage
Network Functions (firewall, DPI, load balancer, etc)
Resource Facing Services
Customer Facing Services
Vendor and implementation independent API
Provisioning: Focus on provisioning process
Activation: Focus on technical implementation

## Slide 10: Historically, the industry has done a poor job bridging fulfilment and assurance

## Slide 11: Although not a focus this week…assurance is changing And modeling has a central part on it

## Slide 12: Coming back, what is a service?
We will focus on “Network Services” which are objects exposed by the provisioning and activation layers to the rest of the fulfillment stack

## Slide 13: What about model driven?
Notes: The word “service” is

## Slide 14: What we have done so far when designing network services
Service design is still a very rudimentary and manual process
In most entities, organizations create text documents with network service descriptions
There is little formality on network services design processes
Automation is not wide-spread. It is also typically done by proprietary systems based on “statements of work”

## Slide 15: What would change with model-drive?
Model-driven systems provides a formalization of the design process, where human-readable objects can now also be read by machines
It requires a modeling language
Three part of a network service that may be influenced by models: inputs accepted by the system, outputs from the systems and the business logic.
Business Logic
INPUT
OUTPUT

## Slide 16: Orchestration
Is the implementation of the business logic
Happens at both layers: Provisioning (customer-facing) and Activation (resource-facing)
Categories:
  Workflow-based orchestration
  Transactional (or intent) -based orchestration
Functions (service lifecycle):
  Design and Assign
  Service decomposition
  Minimum changes calculation and execution
  Recovery (rollback)
  SLA management
Primitives:
  Basic: Create, Read, Update, Delete (CRUD)
  Advance: Re-deploy, Un-deploy, Check-sync

## Slide 17: What will you learn during this class?
You will understand the current challenges facing the traditional network services
You will learn about model-driven architectures as a way to address these challenges
You will learn about YANG, the modeling language from the IETF
You will learn about how to use YANG to model network services

## Slide 18: Network Services Challenges

## Slide 19: Challenges are not just technological New customer behavior and new business models
Execution at the speed of software
Agility, DevOps, NFV, SDN, new services platforms
Rapidly changing business models
Cloud, virtualization, programmable networks
New ecosystems and value chains
OTT co-opetition
Changing customer behavior and new expectations
Everything on demand
New services with a press of a button
All of this requires successful, flexible automation,
but complexity has destroyed many automation initiatives.

## Slide 20: Network Function Virtualization
NFV is the process to move network functions from dedicated hardware to general purpose x86 computers
The technology change is evolving since an original proposal in 2008
NFV involves technology disruptions for:
  Data Plane: making x86 based forwarding suitable for SP services
  Control Plane: new paradigms with highly distributed systems
  Security Plane: shared resources adds new security requirements
  Management Plane: automation is not longer optional for NFV
NFV is happening at both SP and Enterprises

## Slide 21: ETSI MANO Protocol Stack
NFVO has two functions:
  Service Orchestration (SO)
  Resource Orchestration (RO)
NFVO-VNFM has two operation modes:
  Direct
  Indirect
VIM is decouple in two elements:
  VIM Compute (Openstack or Vmware)
  VIM Network (SDN-DC)
Data models and APIs not yet standardized

## Slide 22: NFV is not alone in the virtualization trend
PNF
NFVI
VNF
VIM
Orchestrated
Service Assurance
End To End Network Service Orchestration
NFVO
VNFM
EMS
Controller
EMS
Day1/Day 0 Automation
OSS /BSS
Business Service Orchestration
Portal
End To End DC application and Cloud Orchestration
Telco Cloud & Network Orchestration
Application, DC & Cloud Orchestration
Original slide from Laurent Desauney

## Slide 23: NFV Use cases
Virtual Managed Services:
  Yes, plain old VPNs with added value services: firewall, DPI, content security
  Virtual functions can be dedicated or shared, located in a central DC or distributed at the customer’s CPE (universal CPE)
  One important use case is to save SP expensive MPLS links and move traffic toward Internet
Virtual Packet Core:
  Corporate APN, Machine to machine, IoT…all benefit from dedicated VPCs.
Infrastructure virtualization:
  Virtual route-reflector, virtual BNG, virtual CMTS

## Slide 24: Software Defined Networks (SDN) Not one but three clear technology trends
SDN - DC
Network splicing and service chaining in the DC
SDN - WAN
“Intelligent” WAN solutions for managing branches
Either managed services (adopted by ISPs) or over-the-top with cloud management
SDN - Transport
SP-centric solution to improve resource utilization in its network
Optionally multi-layer
Overlay solutions (VXLAN)
Mainly proprietary solutions
Extending to SP POPs
Mainly management plane focus
Enabled by protocols such as: Segment-Routing, PCEP, BGP-LS and NETCONF/YANG
Network Service Headers (NSH) getting traction
Mostly proprietary solutions with proprietary hardware
All about reduring MPLS costs

## Slide 25: SDN moves Network to ”close-loop control principle”
Network
Analytics
Activation
Centralized controller with overall network knowledge
Topology
Telemetry
“knowledge”
configuration
configuration
Provisioning
Machine-learning in the latest buzz
word

## Slide 26: OpenSource: challenging standard bodies? Is reading code replacing documentation?
And more and more missing ….

## Slide 27: We come back to the people… What is DevOps?
http://dev.mobify.com/blog/devops-101-best-practices/
“The cool-kids way of stringing stuff together with shell scripts.
It exists because we can now wrap things in shell scripts that we used to only dream of; the world is now programmable at a much larger scale, and we have many new tools and techniques for taking advantage of it.”
Takes a new or enhanced feature all the way to production—everyone is adding value to the customer
A method that stresses communication, collaboration, integration, automation, and cooperation across organizational units to deliver features quickly and efficiently.
Based on lean and agile principles
DevOps is the marrying of process, infrastructure, and product

## Slide 28: DevOps
Underpinning: Automation
People, Process Culture
Practices
Tools
DevOps for Networking, Use Things You Can Program, and Program the Things You Use. Stefan Vallin, Cisco

## Slide 29: Changes in Network Professionals’ Skills
An increased knowledge of other IT disciplines
More knowledge of the business
More understanding of applications
More emphasis on programming
Stallings: Foundations of Modern Networking: SDN, NFV, QoE, IoT, and Cloud

## Slide 30: The resulting scenario
From NFV/SDN World congress 2016

## Slide 31: Module 1 Summary
Complexity is on the rise
Requirements are also on the rise
Formalizing the service design, testing and operation process is paramount