## Slide 1: NETCONF and RESTCONF
Roque Gagliano

## Slide 2: Origins of NETCONF and YANG (the Beginning)
Several meetings at events in 2001 (NANOG-22, RIPE-40, LISA-XV, IETF 52)
  Operators expressing opinion that the developments in IETF do not really address requirements configuration management.
June of 2002, the Internet Architecture Board (IAB) held invitational workshop on Network Management [RFC3535] to
  Identify a list of technologies relevant for network management with their strengths and weaknesses
  Identify the most important operator needs.

## Slide 3: RFC 3535: Results from IAB Workshop

## Slide 4: RFC3535: Operator requirements for a new configuration protocol
Ease of use
Separation between configuration and state data
Ability to compare across-devices, across-vendors
Service and network management, not device management
Network-wide transactions
Devices figure out order of commands(ACID…anyways)
No unnecessarily changes
Backup/restore configuration
Validation of configuration
Standardized data models
Support for multiple configuraiton sets
Delayed, orchestrated activation
Role-based access control

## Slide 5
Cost and complexity
Cost
Information leakage
Lack of atomicity
Ordering problem
OSS
NMS
EMS
Implications of RFC 3535, legacy situation

## Slide 6
Reduced
Cost and complexity
Cost/
Value
Require transactions
OSS
NMS
EMS
Implications of RFC 3535, with transactions

## Slide 7: Best Practices Coming Together
SNMP Experience
CLI Best Practices
Operator Requirements
NETCONF and YANG

## Slide 8: YANG – A Data Modeling Language for Networking
Human readable, and easy to learn representation
Hierarchical configuration data models
Reusable types and groupings (structured types)
Extensibility through augmentation mechanisms
Supports definition of operations (RPCs)
Formal constraints for configuration validation
Data modularity through modules and sub-modules
Well defined versioning rules
Why you should care:
YANG is a full, formal contract language with rich syntax and semantics to build applications on

## Slide 9: YANG standard models
Base document: RFC 6020
YANG + NETCONF: RFC 6241
IETF approved documents:
  Common types (RFC 6991)
  IANA Interface types (RFC 7224)
  Interface management (RFC 7223)
  IP management (RFC 7277)
  System management (RFC 7317)
  IPFIX configuration (RFC 6728)
  SNMP configuration (RFC 7407)
In the making:
  Syslog configuration
  ACL configuration
  Network topology, L3 topology
  BGP, OSPF
  Netconf monitoring, Netconf access control (NACM)
  L2VPN, PIM, MPLS-LDP,
Standard content library still small but rapidly growing
Most foundational models are in place
Complement “top-down” definitions with models that are synthetically generated (think Google Translate)

## Slide 10: NETCONF Protocol Introduction

## Slide 11: NETCONF – A Protocol to Manipulate Configuration
IETF network management protocol
Distinction between configuration and state data
Multiple configuration data stores (candidate, running, startup)
Configuration change validations
Configuration change transactions
Selective data retrieval with filtering
Streaming and playback of event notifications
Extensible remote procedure call mechanism
NETCONF Notifications support
New work on pushing pub/subs to expand NETCONF into telemetry
Why you should care:
NETCONF provides the fundamental programming features for comfortable and robust automation of network services

## Slide 12
Self-service portal
Call center
Products & Price Catalog
Order capture engine
Customers & accounts
Product configuration
Order Management
Service provisioning
Service activation
Supply Chain
Field Service
Installed assets
Billing
Customer care
Knowledge
base
Contracts & SLAs
CPQ
Service Fulfillment and related parts of OSS/BSS (except Service Assurance)
Resource inventory
Notes: CPQ = Configure, Price and Quote

## Slide 13: What is NETCONF?
NETCONF (Network Configuration Protocol) is an IETF configuration management protocol
  not only config access, also operational state data
  NETCONF uses XML (as you are going to see)
Why NETCONF?
Easy to Use
Separates Config and Operational Data
Lots of Tooling
Accessible Format
Error Checking
Backup/Restore Capability
Human and Machine Friendly
Next-Gen Configuration Management Requirements
RFC3535

## Slide 14: What is an ACID transaction
Atomicity:
  Transactions are indivisible, all-or-nothing
Consistency:
  Transactions are all-at-once
  There is no internal order inside a transaction, it is a set of changes, not a sequence
Independence:
  Parallel transactions do not interfere with each other
  Transactions appear to happen always-in-sequence
Durability
  Committed data always-sticks, i.e. remains in the system even in the case of a fail-over, power failure, restart, etc

## Slide 15: NETCONF IETF Standard Information
V 1.0 | V 1.1 | Extension
RFC 6535 Background and Requirements | RFC 6241 1.1 Base NETCONF Protocol | RFC 5277 Notifications
RFC 4741 1.0 Base NETCONF Protocol | RFC 6242 NETCONF over SSH | RFC 5717 Partial Locking
RFC 4742 NETCONF over SSH |  | RFC 6243 With defaults
 |  | RFC 6244 NETCONF + YANG Architectural Overview

## Slide 16: NETCONF Protocol Stack
Transport
Messages
Operations
Content
Server
Client
SSH
Reason:
Connection-oriented (TCP)
Authenticated
Reliable
Secure
Client initiated session

## Slide 17: NETCONF Protocol Stack
Transport
Messages
Operations
Content
Server
Client
<rpc>
RPC Client’s Request Methods:
Controller
NMS
Script
Manual
<rpc-reply>
NETCONF Messages:
Remote Procedure Call (RPC)

## Slide 18: NETCONF Protocol Stack
Transport
Messages
Operations
Content
OPERATION | DESCRIPTION
<get-config> | Retrieve data from the running configuration
<get> | Retrieve running configuration or device statistic
<edit-config> | Modify a configuration database operation = merge (default), delete, create, replace, remove test-option (:validate), error-option
<copy-config> | Copy a configuration database
<delete-config> | Delete a configuration database
<commit> | Commit candidate configuration to the running db
<lock>/<unlock> | Lock or unlock a configuration datastore system
<close-session> | Terminate this session
<kill-session> | Force Termination of session
<create-subscription> | event notification subscription
<notification> | asynchronously message from server to client when an event of interest has occurred

## Slide 19: NETCONF Protocol Stack
Transport
Messages
Operations
Content
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>
urn:ietf:params:netconf:base:1.0
</capability>
<capability>
urn:ietf:params:netconf:capability:candidate:1.0
</capability>
<capability>
urn:ietf:params:netconf:capability:notification:1.0
</capability>
</capabilities>
<session-id>285212672</session-id>
</hello>
]]>]]>

## Slide 20: NETCONF Configuration Data Stores
Named configuration stores
  Each data store may hold a full copy of the configuration
Running is mandatory, Startup and Candidate optional (capabilities :startup, :candidate)
Running may or may not be directly writable (:writable-running)
  Need to copy from other stores if not directly writable
Startup
Running
Candidate
Files… / URLs…
Notes: Candidate is required for network wide transactions

## Slide 21: NETCONF Call Flow (1)
1) Client sends HELLO message to Server. It includes its Capabilities.
>>>>out 16-Dec-2016::14:25:02.051 device=pe2
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities><capability>urn:ietf:params:netconf:base:1.0</capability><capability>urn:ietf:params:netconf:base:1.1</capability></capabilities>
</hello>

## Slide 22: NETCONF Capabilities exchange
Allows extensibility of the protocol
Are transmitted in the ”hello” message and set what each party is capable of:
  Some from NETCONF standards
  Each YANG modules supported by the server is also a capability. YANG modules include revision number
  Other extensions
The manager uses the capabilities to determinate what operations can send to the server

## Slide 23: NETCONF Capabilities
:writable-running!
:candidate!
:confirmed-commit!
:rollback-on-error!
:validate!
:startup!
:url (scheme=http, ftp, file, …)
:xpath (filters)
Optional Capabilities (RFC 6241)
Other Capabilities
:notification, :interleave (RFC 5277)
:partial-lock (RFC 5717)
:with-defaults (RFC 6243)
:ietf-netconf-monitoring (RFC 6022)
And you can define your own, like
:actions (tail-f)
:inactive (tail-f)

## Slide 24: NETCONF Call Flow (2): Hello from server
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.0</capability>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:candidate:1.0</capability>
<capability>urn:ietf:params:netconf:capability:confirmed-commit:1.0</capability>
<capability>urn:ietf:params:netconf:capability:confirmed-commit:1.1</capability>
<capability>urn:ietf:params:netconf:capability:xpath:1.0</capability>
<capability>urn:ietf:params:netconf:capability:validate:1.0</capability>
<capability>urn:ietf:params:netconf:capability:validate:1.1</capability>
<capability>urn:ietf:params:netconf:capability:rollback-on-error:1.0</capability>
<capability>http://tail-f.com/ns/netconf/with-defaults/1.0</capability>
<capability>http://tail-f.com/ns/netconf/actions/1.0</capability>
<capability>http://tail-f.com/ns/netconf/extensions</capability>
<capability>urn:ietf:params:netconf:capability:with-defaults:1.0?basic-mode=explicit&amp;also-supported=report-all-tagged</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-with-defaults?revision=2011-06-01&amp;module=ietf-netconf-with-defaults</capability>
<capability>urn:ietf:params:netconf:capability:yang-library:1.0?revision=2016-06-21&amp;module-set-id=c9f8a470ce0ddaa46d30ed57fae7d5bb</capability>
<capability>http://xml.juniper.net/xnm/1.1/xnm?module=junos</capability>
<capability>urn:ietf:params:xml:ns:yang:iana-crypt-hash?module=iana-crypt-hash&amp;revision=2014-08-06&amp;features=crypt-hash-sha-512,crypt-hash-sha-256,crypt-hash-md5</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-monitoring?module=ietf-netconf-monitoring&amp;revision=2010-10-04</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-notifications?module=ietf-netconf-notifications&amp;revision=2012-02-06</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-restconf-monitoring?module=ietf-restconf-monitoring&amp;revision=2016-08-15</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-yang-library?module=ietf-yang-library&amp;revision=2016-06-21</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-yang-types?module=ietf-yang-types&amp;revision=2013-07-15</capability>
<capability>urn:juniper-rpc?module=junos-rpc</capability>
</capabilities>
<session-id>13</session-id></hello>]]>]]>

## Slide 25: NETCONF Call Flow (3): Lock in candidate
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”1">
<lock><target><candidate/></target>
</lock>
</rpc>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”1"><ok/></rpc-reply>

## Slide 26: NETCONF Call Flow (4): Edit Config
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”2">
<edit-config xmlns:nc='urn:ietf:params:xml:ns:netconf:base:1.0'><target><candidate/></target><test-option>test-then-set</test-option><error-option>rollback-on-error</error-option><config>
<configuration xmlns="http://xml.juniper.net/xnm/1.1/xnm"><system><host-name>curso_mvdeo</host-name></system></configuration></config></edit-config>
</rpc>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”2"><ok/></rpc-reply>
Notes: <?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="4"><ok/></rpc-reply>

## Slide 27: NETCONF edit-config
nc:test-option (:validate)!
test-then-set (default)
set!
test (:base:1.1)!
nc:error-option!
stop-on-error (default)
continue-on-error!
rollback-on-error (:rollback-on-error)!
nc:operation!
merge!
replace!
create!
delete !  Error if item does not exists
remove (:base:1.1)!  No error if item does not exists

## Slide 28: NETCONF Call Flow (5): Confirmed commit
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”3">
<commit><confirmed/>
</commit>
</rpc>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”3"><ok/></rpc-reply>

## Slide 29: NETCONF Call Flow (6): Commit
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”4">
<commit/></rpc>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”4"><ok/></rpc-reply>

## Slide 30: NETCONF Call Flow (7): Close session
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”5">
<close-session/></rpc>
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id=”5"><ok/></rpc-reply>
Note: You can also “kill” a session (not that polite)

## Slide 31: NETCONF Protocol Stack Summary
Config data, Notification (XML)
Transport
Messages
Operations
Content
<get>, <get-config>,<edit-config> etc
<rpc>, <rpc-reply>
SSH
Client
Server

## Slide 32: NETCONF Opensource tools
  Python NETCONF Client library: https://github.com/ncclient/ncclient
Java NETCONF Client library: https://github.com/tail-f-systems/JNC
C NETCONF Client library: https://github.com/CESNET/libnetconf
More: http://www.netconfcentral.org/

## Slide 33: ResTful:Representational state transfer
Characteristics
  Stateless operations: server does not keep any state between requests
  Textual representation: typically JSON or XML
  Resources specified in URI
  Pre-defined Verbs: GET, POST, PUT, DELETE, PATCH, …
ReSTful gained popularity because:
  Performance
  Scalability
  Simplicity
  Portability

## Slide 34: ResTful does not mean “standard API” And “documented” is not “open”
Vendors are now exposing ResTful configuration APIs
The problem is that every API differs on:
  HTTP options
  Authentication
  Verbs interpretation
  Encoding
  Etc.
The conclusion is that a “Driver” is still needed for every configuration devices
In general, the Swagger Specification (from OpenAPI project) is addressing the documentation problem
For CRUD operations, the IETF defined RESTCONF using YANG modeling language

## Slide 35: RESTCONF - Standard HTTP-based configuration protocol
Still an emerging story (at IETF queue)
RESTful protocol to access YANG defined data
Representational State Transfer, i.e. server maintains no session state
URIs reflect data hierarchy in a Netconf datastore
HTTPS as transport
Data encaded with either XML or JSON
Operations

## Slide 36: NETCONF and RESTCONF are not equal
RESTCONF does not have concept of transaction across calls and therefore cannot implement “network wide transactions”
Some operations missing:
  There is no “Validate” call in RESTCONF
  Missing “copy-config”
NOTIFICATION support in RESTCONF depends on W3C event streaming recommendation (not widely available)

## Slide 37: Some RESTCONF features
MUST support TLS and MUST NOT be used without TLS support (mandatory security)
Authentication: password (HTTP auth.) or client-certificate
Resources:
  Root Resources Discovery available (for exampel /restconf)
  Media types: JSON and XML encoding supported
  API Resources ({+restconf}/…):
Child Resource | Description
data | Contains all data resources
operations | Data-model-specific operations
yang-library-version | ietf-yang-library module date

## Slide 38: Example DATA Operations Retrieving Server capabilities
GET /restconf/data/ietf-restconf-monitoring:restconf-state/\ capabilities HTTP/1.1 Host: example.com Accept: application/yang-data+xml
HTTP/1.1 200 OK Date: Mon, 23 Apr 2016 17:02:00 GMT Server: example-server Cache-Control: no-cache Last-Modified: Sun, 22 Apr 2016 01:00:14 GMT Content-Type: application/yang-data+xml Bierman, et al. Expires April 30, 2017 [Page 115] Internet-Draft RESTCONF October 2016 <capabilities xmlns="urn:ietf:params:xml:ns:yang:ietf-restconf-monitoring"> <capability>\ urn:ietf:params:restconf:capability:defaults:1.0?\ basic-mode=explicit\ </capability> <capability>\ urn:ietf:params:restconf:capability:with-defaults:1.0\ </capability> <capability>\ urn:ietf:params:restconf:capability:depth:1.0\ </capability> <capability></capabilities>

## Slide 39: Example DATA Operations Creating a new resource
POST /restconf/data/example-jukebox:jukebox/library HTTP/1.1 Host: example.com Content-Type: application/yang-data+json
{
"example-jukebox:artist" : [
{
"name" : "Foo Fighters"
} ]
}
HTTP/1.1 201 Created Date: Mon, 23 Apr 2016 17:02:00 GMT Server: example-server Location: https://example.com/restconf/data/example-jukebox:jukebox/library/artist=Foo%20Fighters Last-Modified: Mon, 23 Apr 2016 17:02:00 GMT ETag: "b3830f23a4c"
module example-jukebox {
namespace "http://example.com/ns/example-jukebox";
prefix "jbox";
container jukebox {
list artist {
key name;
leaf name { type string { length "1 .. max"; }
}
}}
YANG
RESTCONF Query
RESTCONF Response

## Slide 40: Example Operation Resource
module example-ops {
namespace "https://example.com/ns/example-ops";
prefix "ops";
rpc reboot {
input {
leaf delay { units seconds; type uint32; default 0; }
leaf message { type string; }
leaf language { type string; } }
}
rpc get-reboot-info {
output {
leaf reboot-time { units seconds; type uint32; }
leaf message { type string; }
leaf language { type string; }
}
}
}

## Slide 41: Example Operation Resource
POST /restconf/operations/example-ops:reboot HTTP/1.1 Host: example.com Content-Type: application/yang-data+json
{ "example-ops:input" :
{
"delay" : 600,
"message" : "Going down for system maintenance",
"language" : "en-US"
}
}
HTTP/1.1 204 No Content Date: Mon, 25 Apr 2016 11:01:00 GMT Server: example-server

## Slide 42: Example Operation Resource
POST /restconf/operations/example-ops:get-reboot-info HTTP/1.1 Host: example.com Accept: application/yang-data+json
HTTP/1.1 200 OK Date: Mon, 25 Apr 2016 11:10:30 GMT Server: example-server Content-Type: application/yang-data+json
{
"example-ops:output" : {
"reboot-time" : 30,
"message" : "Going down for system maintenance",
"language" : "en-US"
}
}